## Slide 2
FUN & LEARNING
Canpisce

## Slide 3
8.00 to 8.10
Attendance
9.45 to 10.00
Rest Time
12.00 to 13.30
Lunch Time
15.40 to 16.00
Rest Time
15.40 to 16.00
Rest Time
Time Frame

## Slide 4
LAT Objectives
What is LEAN ?
LEAN History
Why LEAN
5 Gen’s
LEAN Principles
Just in Time
Takt Time
Pull System
Jidoka
Kiazen 3-1-3
1St Session
OUTLINE

## Slide 5
LEAN Tools
Value Stream MAP
Process Flow Chart
Spaghetti Diagram
Pareto
Histogram
Ishikawa Diagram, 5 whys analysis
Brainstorming
Poka Yoke
SMED
Kanban
Visual Control
Ergonomic Principles
Standard Work
Control Mechanism
2nd Session
OUTLINE

## Slide 6
Canpisce
LAT OBJECTIVE
1st Session
Understand LEAN Principal
Knowing the benefits of LEAN
Able to run Kiazen effectively
Apply LEAN Tools Appropriately

## Slide 7
Learning Together
Observe/Exposure
Learn
We Know What we Know
We Don’t’ Know What we Don’t Know
We Know What we Don’t Know
We DO Know What we Know
We Don’t’ Know What we Don’t Know
We DO Know What we Know
LEAD
DIRECT
GUIDE
Coaching Mentoring
We Know What we Know
Key To Success

## Slide 8
Give a MAN a FISH, and you feed him for a day
Show him how to catch a fish, and you feed him for a lifetime.

## Slide 9
LEAN Integration into Operation
Operation Lean Leader Lead the dedicated PEOPLE (vital view)
to drive employee (All) continuously with Lean approach
Current Condition
JDI Approach
Daily Management approach for managing
6S Approach
TPM Approach
We Are Here
Kaizen 3-1-3
LEAN
Operation Activities Performance

## Slide 10
Kaizen Operation Performance
Leadership Characteristics
Technical Knowledge Skills Set
Lean Knowledge Experience
Leader to practice LEAN and be a coach
Technical know how on process Not just what happen
Individual Coach competency to drive Lean concept to Applications
Operation Performance
LEAN TRANFORMATION
LEAN Leader Characteristics
Kaizen Team Competency

## Slide 11
Canpisce
What is LEAN ?
1st Session
Create Value for Customer Eliminate MUDA (Waste)

## Slide 12
LEAN History
1900
Just in Time
Toyoda Automatic Loom patented with JIDOKA Mechanism
Kiichiro Toyoda
Founds Toyota Motor Corporation
Sakichi Toyoda invents Toyoda model G Automatic Loom
PULL System Established
Toyota lays off 1,600 workers narrowly avoiding
Bankruptcy
KICHIRO TOYODA RESIGNS
Eiji Toyoda visits
Ford Plant
at Rounge River
1st Arab Oil Embargo
Shingeo Shingo
Visits USA
Former Ohno disciples
Begin consulting
In USA
1950
Supermarket System
Shingeo Shingo advises Toyota on setup Time reduction
Taiichi Ohno organizes group to tech TPS to
Supplier
Toyota suffers massive loss of customer trust due to safety problems
Toyota suffers Losses following the Lehman Brothers collapse
AKIO Toyoda announces
TOYOTA GLOBAL VISION
2000

## Slide 13
" A systematic approach to identity and eliminating waste (Non-Value added Activities) , while providing Product or Services based on customer request (Pull System), through KAIZEN , in pursuing toward perfection."
LEAN Definition
MEP LEAN Network

## Slide 14
Why Need LEAN
LEAN APRROACH
TRADITIONAL APPROACH
Price
Cost
Profit
Price
Cost
Profit

## Slide 15
Why Need LEAN
TRADITIONAL APPROACH
HOW ?
PRICE
USD500
Production Cost
USD 300
Profit
USD200
PRICE
USD300
Production Cost
USD 300
Profit USD 0
LEAN
APPROACH
PROFIT
USD200
PRICE
USD300
PRODUCTION COST
USD100

## Slide 16
Why Need LEAN
LEAN APRROACH
TRADITIONAL APPROACH
Price
Cost
Profit
Price
Cost
Profit

## Slide 17
Finding
the Difference
in 10 Mins

## Slide 18
What the Sensei Say……
“Genchi Genbutsu”
GO See
Part of Daily Management ‘s Important Focus

## Slide 19
“DATA from the report is Important, but I put more emphasis on the facts looking myself”
-Taiichi ohno

## Slide 20
5 Gen’s
GENBA
GENBUTSU
GENJITSU
GENRI
GENSOKU
Go to the “Actual Price”
Look at the “Actual Thing”
Find the
“Actual Fact”
Use the
“Actual Theory /Knowledge”
Understand the “Actual Current Standard”

## Slide 21
Go to Paper Machine -2
Analyze at the defective Paper roll Produced
See the Actual Machine Setting
Paper Roll Wrinkles
(Defect)
Understand and Apply the Paper Production theory
Know the Rules /SOPs used for setting Paper Machines
EXAMPLE

## Slide 22
GENBA WALK
NORMAL
IMPROVE
ABNORMAL
ROOT CAUSE
ACTION
NOT JUST WALK !!!!
observe
GENCHI GENBUTSU

## Slide 23
GENBA WALK
NORMAL
IMPROVE
ABNORMAL
ROOT CAUSE
ACTION
NOT JUST WALK !!!!
observe
GENCHI GENBUTSU

## Slide 24
WHAT Aspect to Focus ?
Safety
Unsafe conditions and unsafe behavior
Performance
The Practice deviates from the currently defined standard (SOP/WI/SW)
MUDA
Practice with 7 Waste of Waste (Time wood)
Revise SOP/WI/SW if applicable
Create SOP/WI/SW if not available
Transportation
Motion
Inventory
Defects
Waiting
Overproduction
Over processing
M
U
D
A

## Slide 25
What Aspects to Focus ?
MAN
Daily Activities : Look
MATERIAL
What are kept or stored : Look
MACHINE
Operating Performance : Heard, Look, Smell, Feel
METHOD
Any Activities by man, Machine, Equipment Look
MOTHER NATURAL (ENVIRONMENT)
Actual or Potential impact to Surrounding : Look, Smell
MEASUREMENT
What Should be the Target : Look

## Slide 26
High Potential fall in
Sealing water not functioning
Pump overflow
High Potential Trip Over
Malfunction Meter
Water Discharge
SAFETY
PERFORMANCE
MUDA
EXAMPLE

## Slide 27
What is Value
Value is the product /Service specification required by the customer that they willing to pay for their intended to use
Value activity
Process activity carried out by a person or machine, through changing the form or function of the product /service that meet what is needed by the customers
CREATE VALUES FOR CUSTOMERS

## Slide 28
Non Value Added Activates - WASTE (MUDA)
Value Enabler Activates -Needed for internally
Value Added Activates - Needed for Customers
Activities Category

## Slide 29
Motion
Inventory
Defects
Waiting
Transportation
Overproduction
Over
processing
Value Added
Locally and Globally ordinary organizations contain at least 70% waste in their business
7 MUDA (Wastes)
What is Our level of MUDA?

## Slide 30
That is caused by the process of transporting /moving goods / materials
in a process using a vehicle that does not help provide the required value
Transactional
Paper-based data transfer instead of Electronic.
Inter-Office Mail routing for unnecessary approvals /Processing.
Operational
Forklifts, Conveyors Long travel distance unplanned premium freight
Large batch containers.
MUDA of Transportation

## Slide 31
My Price is cheaper .....come and Buy Me
My Price is more expensive because My RAW Materials come from places far from the factory
$29
$35
EXAMPLE

## Slide 32
That is caused by the accumulation of excessive material with no demand, where the Materials tie up CASH(money)
TRANSACTIONAL
Excessive backlog of work to be processed.
Too Much Paper to be handled processed & filled.
Operational
Making what we can instead of what customer needs.
High obsolescence & write offs
MUDA of Inventory

## Slide 33
MUDA of Motion
That is caused by the movement of the human body which does not add
value to the Raw materials in the process of becoming finished goods
TRASACTIONAL
Walking to deliver Paperwork,
Poor ergonomic work space,
Chasing needed information or Data
OPERATIONAL
Repetitive and unnecessary movement of parts and people caused by poor ergonomic design

## Slide 34
MUDA of Waiting
TRANSACTIONS
Waiting for meeting to start
Waiting for information, paper works, approvals
OPERATIONS
Waiting for machines to cycle,
Waiting for materials & tools
This type of MUDA is the most happening because it is not visible in plain sight
Time spent with no activity at all on the material & Transaction

## Slide 35
MUDA for Overproduction
This is caused by too much production compare to market & subsequent downstream demand.
TRANSACTIONS
Too many reports, reviews, approvals, paperwork. Doing more than its needed
OPERATIONS
Running machines and making parts to keep the machines and people busy
To fill up machines capabilities and not customer demand

## Slide 36
Is this Good ?
EXAMPLE

## Slide 37
MUDA for Over processing
Caused by excessive work steps to achieve the required result or provide what customer not needed in term of specification
TRANSACTIONS
Various approvals
Multiple Checking
OPERATIONS
Incapable machines and processes.
Providing features or function not needed

## Slide 38
MUDA for Defect
Product or service that does Not meet customer requirements
TRANSACTIONS
Missing information
Rework, lost time, mistakes
OPERATIONS
Scrape, rework, lost capacity due to process issues, inaccurate or missing standards operating procedures.

## Slide 39
Use 1
DAY……….
New replacement only can be delivery after 1 week
Is This Good ?
Example

## Slide 40
Think and Write down the types MUDA Experienced at least give one Example for each category
MOTION ?
Waiting?
Defect?

## Slide 41
Operator | Standard Work | Takt Time Production
Material | Standard work in process KANBAN | One Piece Flow Supermarket
Machine | ANDON operational availability | Pull System
Just-in-time To make product at a time at good timing when it is sold
JIDOKA (Autonomation) Stop at every Abnormality
R.P.S. – REG Production System
H E I J U N K A
Cost reduction through elimination of MUDA (Waste or Non – Value Added work)
LEAN House

## Slide 42
Production Levelling
Known as HEIJUNKA (Japanese), tackling High Variation production demand
Which means “Distribution of production volume and stirring evenly”
HEIJUNKA converts the inequality of pull customers into an even and predictable manufacturing process
HEIJUNKA is generally used in conjunction with other LEAN principles to stabilize the flow of values
Week | Total Demand
1 | 4878
2 | 3672
3 | 4536
4 | 4230
5 | 3618
6 | 4788
7 | 4464
8 | 3996
9 | 3546
10 | 4356
11 | 4536
12 | 3888
Weekly Leveled Production (4 week Leveling)
4329
4329
4329
4329
4217
4217
4217
4217
4082
4082
4082
4082
17,316
4
4,329
16,866
4
4,217
16,326
4
4,082

## Slide 43
Production Leveling
Week
1
2
3
4
5
6
7
8
Product leveling
By Product Type
We Make A’s, B’s and C’s
Week
1
2
3
4
5
6
7
8
Batching
extended download for machine conversions. Worker go Home Early.
Customer waiting for Product A is tired od Waiting. Goes another Supplier.
Conversion times are reduced and machines are flexibility tooled.
Customers are Happy with steady and Predictable flow of Product. Workers are happy with even work flow.

## Slide 44
Product - A
Product - B
Product - C
Product - D
Product - E
Product - F
Pitch for setting the process period
Production scheduling and checking in each pitch
Heijunka Box
KANBAN card –
Qty & time to produce
One Column/Pitch
Load Levelling Box - Heijunka Box

## Slide 45
Produce only what is needed, when it is needed, and in the right amount and right quality needed
Just-In-Time - JIT

## Slide 46
Reliable equipment & Machines
Well designed work cells
Quality improvements
Standardized operations
Pull production
Single piece flow & flow at the beat of Customer
Requirements for implementing JIT

## Slide 47
Borrowed from German word Taktzeit.
It's a "Production Heartbeat" with purpose is to adjust the speed of Production market Demand.
TAKT
TIME
Available Time
Total Customer Demand
TAKT TIME

## Slide 48
CYCLE TIME
The total time needed to complete 1 (One) series of work/Tasks from start to finish
End Goal : Cycle Time
Takt Time

## Slide 49
40
38
36
34
32
30
28
26
22
24
20
18
16
14
12
10
8
4
0
2
Quality check
39
24.1
13.8
6.9
34
25.3
Takt
Time
Operator-1
Take body case, locking nut
Operator-2
Take back grille and tapping screw
Operator-3
Take blade and blade holder
Operator-4
Assembly
Operator-5
Take front grille & cover
Operator-6
OPERATOR
TIME (Second)
CYCLE TIME
Example Load Chart
Tighten
Using Locking Nut
Put
Power
Cord
Assembly
Assembly
Find Assembly
What are the Abnormalities ?
What are the action ?

## Slide 50
Total Time required by the specific Unit to be careful from position A to Position B
Customer Request
Customer Receive
CYCLE TIME
LEAD TIME
B
A
Manufacturing
LEAD Time

## Slide 51
PULL System

## Slide 52
PUSH System
Raw Material
Inventory
WIP
Waiting
WIP
Assembly
Long Cycle Time
Production Control
Turning
Waiting Receive
Customer

## Slide 53
Operator | Standard Work | Takt Time Production
Material | Standard work in process KANBAN | One Piece Flow Supermarket
Machine | ANDON operational availability | Pull System
Just-in-time To make product at a time at good timing when it is sold
JIDOKA (Autonomation) Stop at every Abnormality
R.P.S. – REG Production System
H E I J U N K A
Cost reduction through elimination of MUDA (Waste or Non – Value Added work)
LEAN HOUSE

## Slide 54
Production Levelling
Known as HEIJUNKA (Japanese), tackling High Variation production demand
Which means “Distribution of production volume and stirring evenly”
HEIJUNKA converts the inequality of pull customers into an even and predictable manufacturing process
HEIJUNKA is generally used in conjunction with other LEAN principles to stabilize the flow of values
Week | Total Demand
1 | 4878
2 | 3672
3 | 4536
4 | 4230
5 | 3618
6 | 4788
7 | 4464
8 | 3996
9 | 3546
10 | 4356
11 | 4536
12 | 3888
Weekly Leveled Production (4 week Leveling)
4329
4329
4329
4329
4217
4217
4217
4217
4082
4082
4082
4082
17,316
4
4,329
16,866
4
4,217
16,326
4
4,082

## Slide 55
PRODUCTION LEVELING
Week
1
2
3
4
5
6
7
8
Product leveling
By Product Type
We Make A’s, B’s and C’s
Week
1
2
3
4
5
6
7
8
Batching
extended download for machine conversions. Worker go Home Early.
Customer waiting for Product A is tired od Waiting. Goes another Supplier.
Conversion times are reduced and machines are flexibility tooled.
Customers are Happy with steady and Predictable flow of Product. Workers are happy with even work flow.

## Slide 56
Product - A
Product - B
Product - C
Product - D
Product - E
Product - F
Pitch for setting the process period
Production scheduling and checking in each pitch
HEIJUNKA BOX
KANBAN card –
Qty & time to produce
One Column/Pitch
Load Levelling Box - Heijunka Box

## Slide 57
Produce only what is needed, when it is needed, and in the right amount and right quality needed
Just-In-Time - JIT

## Slide 58
Reliable equipment & Machines
Well designed work cells
Quality improvements
Standardized operations
Pull production
Single piece flow & flow at the beat of Customer
REQUIREMENTS FOR IMPLEMENTING JIT

## Slide 59
Borrowed from German word Taktzeit.
It's a "Production Heartbeat" with purpose is to adjust the speed of Production market Demand.
TAKT
TIME
Available Time
Total Customer Demand
TAKT TIME

## Slide 60
CYCLE TIME
The total time needed to complete 1 (One) series of work/Tasks from start to finish
End Goal : Cycle Time
Takt Time

## Slide 61
40
38
36
34
32
30
28
26
22
24
20
18
16
14
12
10
8
4
0
2
Quality check
39
24.1
13.8
6.9
34
25.3
Takt
Time
Operator-1
Take body case, locking nut
Operator-2
Take back grille and tapping screw
Operator-3
Take blade and blade holder
Operator-4
Assembly
Operator-5
Take front grille & cover
Operator-6
OPERATOR
TIME (Second)
CYCLE TIME
EXAMPLE LOAD CHART
Tighten
Using Locking Nut
Put
Power
Cord
Assembly
Assembly
Find Assembly
What are the Abnormalities ?
What are the action ?

## Slide 62
Total Time required by the specific Unit to be careful from position A to Position B
Customer Request
Customer Receive
CYCLE TIME
LEAD TIME
B
A
Manufacturing
LEAD TIME

## Slide 63
PULL SYSTEM

## Slide 64
PUSH SYSTEM
Raw Material
Inventory
WIP
Waiting
WIP
Assembly
Long Cycle Time
Production Control
Turning
Waiting Receive
Customer

## Slide 65
Create 1 piece Flow & PULL
KANBAN Approach to create the PULL
Here it is
I need One
Operation -1
Operation -2
Operation -3
Operation -4
PULL SYSTEM
I need One
Here it is
Here it is
I need One NOW

## Slide 66
Automation = Self moving
自 動 化
Autonomation = Self working
自 働 化
Human Aspect
JI
DOU
KA
AUTONOMATION
Automation with human intelligent
JIDOKA

## Slide 67
Human Intervene Repair
Andon
light
Automatic Feed
Automatic Feed
Automatic Ejection
Watch machine cycle
Manual feed and cycle watch machine cycle
Self –Monitoring Machine
JIDOKA EVOLUTION

## Slide 68
OBJECTIVE
SEPARATING
APPROACH
Enabling operations to build quality in every process.
Separating the Activities of Human from Machine.
The Ability to detect and stop Immediately.
JI
DOU
KA
自 働 化

## Slide 69
4 step of JIDOKA
Canpisce

## Slide 70
4 STEP OF JIDOKA
Machine detect abnormalities.
Machine automatic stop, send out the signal
Human resolve the abnormalities, enable ,machine continue to work.
Human identify the root cause (observe) to derive improvement action ( for frequent repeated problem)
Step 01
Step 02
Step 03
Step 04

## Slide 71
善
Zen
Good (Or Better)
改
Kai
Change
Continuous Efforts to change current conditions/Practice towards perfection
If you think that every think is working as it should, you cannot do Kaizen “
Taiichi Onno, “Father of TPS (Toyota Production System)”
What is KAIZEN ?

## Slide 72
"The message of the Kaizen strategy is that not a day should go by without some kind of improvement being made somewhere in the company."
"Kaizen is everyday improvement, everybody improvement, everywhere improvement.
Kaizen means ongoing improvement involving everybody, without spending much money."
What is Kaizen ?
Masaaki Imai
Kaizen Institute, Ltd.

## Slide 73
Kaizen does not only mean "Continuous Improvement", but Kaizen has a broad meaning , namely:
Self-Discipline
Commitment
Integrity
Not only that , Kaizen must be done
Start with me (Starting with yourself)
Everyday
Everybody
Everywhere
What is Kaizen ?

## Slide 74
Kaizen is not only done by Production or Engineering /Maintenance employee , but Kaizen is
THE WHOLE COMPANY
Although Kaizen is done on the ground, Kaizen must be started by the managers, because they need to lead & Coach as
LEAN LEADERS
What is Kaizen ?

## Slide 75
Efforts to find solutions to reach the targets, not efforts to find excuses why can not reach the targets.
Open- minded - do not blame others, but to be better together.
Commitment and persistent to implement what is decided –sustainable.
RULES OF THUMB

## Slide 76
KAIZEN MINDSET
Changes never end
Abnormalities = Opportunity to excel
Run a solution that has been determined and approved, not to wait until it is perfect

## Slide 77
THINK Creatively to get solutions
"Do Not use Wallet“

## Slide 78
KAIZEN FOCUS ON 3 ASPECTS
TOPICC
Direction/Approach, KPI
SOP/WI/FORM
To manage system
To manage tool
Internal staff at multiple level (behavior, competence, altitude, commitment )
External contractor
Operation Tools
Administrative Tools
to Create, apply (use) to Guide, Manage
To help To Create, Apply (Use)

## Slide 79
KAIZEN Focus on 3 Aspects
Teams and System Thinking
"94%" of Problems in business are systems driven and only 6% are people driven .
W. Edwards Deming
1900-1993

## Slide 80
KAIZEN 3-1-3
Pre Kaizen
3 weeks stared for the preparation.
weeks of Direction, Plan, Analyze, Narrow down
Very Crucial!!!
3
1
3
Kaizen Week
1 Week focus efforts to make the changes happen, achieve the Kaizen target Week of Action
Very Focus !!
Post Kaizen
Up to 3 months to ensure sustainability of Performance Weeks of Monitoring, fine tuning
Very Essential !!

## Slide 81
Identify the opportunities
SMART A3
Current condition Understanding
Pre-Kaizen Activities: Kaizen focus approach, Gemba observation, Fishbone, LAT
Activities pace vs Takt Time setup control
ACT
Sustainability
Activation of Countermeasure of control mechanism
Post Kaizen Monitor include actual pace against Takt Time
Action item completion
Integration into Daily Management
Prioritize focus Decision from Root cause identification
Develop Hypothesis
Test & Proven Hypothesis
Solution Decision Managing
Set New Standard (include control mechanism)
DO
CHECK
IDENTIFY
PCDA IN KAIZEN 3-1-3

## Slide 82
PDCA IN KAIZEN 3-1-3
Kaizen at a Glance
PREP
Previous data
Safety
5S
Quality
Productivity
List of Supplies
Tool Box
Forms
Rules
Snacks
COMMUNICATION
KICKOFF
BURNING QUESTIONS
REPORTS OUT
OPTIONAL TODAY ONLY
WHAT WE DID WHAT’S NEXT FEEDBACK
SHOW & TELL PROPOSED STD. WORK
FINAL PRESENTATION
CELEBRATE
Review Status
STEP-1
STEP-2
STEP-3
STEP-4
FOLLOW THROUGH
PROFILE BIG IDEA
TARGET SHEET
OBSERVE
TRY STORM
IMPLEMENT
STANDARD WORK
POST & REVIEW
STANDARDS WORK
Open Eyes Open Mind
SORT ISSUE
Safety & 5S
Operator Interview
SPAGHETTI MAP
TIME
TIME LINE
Identify waste
Raise Issue
Ask why 5 times
For Impact A or B
“DO ABLE” = 1 OR 2
DIVIDE & CONQUER
MAKE EXPERIMENTS
COMPARE RESULTS TO TARGET MEASURES
IDEA FOR IMPROVEMENT
Stuck
  Ask 7 ways
  Catalyst
  Matrix
Trail Run
Compare Results
Over & Over
Make Adjustments
LOOK FOR BEST
  LEAST WASTE
  SURE QUALITY
  MOST VISIBLE
  SAFETY
  LEVEL”EST” WAY
Time
Space
Make Output Chart
Set up Comment loop
Plan
Actual
Parteo
Kaizen News paper
Open Action Item
PRACTICE FINAL PRESENTATION
Post & Review
Standards Work
Finish – address
Open Action Items
Check for Drift
Select Next
Profile Big Idea
Target Sheet

## Slide 83
A3 FORM

## Slide 84
A3 FORM

## Slide 85
A3 FORM

## Slide 86
A3 FORM

## Slide 87
Roles and Responsibility
Leader and Drive
Lead and Drive
Team Member
Pro-active focus engagement
Secretary
Consolidate, analyze and highlight
Fresh eyes
Challenge at different perception

## Slide 88
Don’t focus executive specific action, allocate time to focus route going around
Each Kaizen sub team
Align Kaizen team direction
Guide Kaizen team action
Provide the decision
Motivate Kaizen team
Driving Kaizen team engagement at all time !!

## Slide 89
A3 FORM

## Slide 90
A3 FORM

## Slide 91
KAIZEN 3+1+3
Pre Kaizen Activity
  Understand customer demand
  Decide project title and scope
  Dedicate compatible person as team member
  Set up baseline and target
  Genba Observation, historical data analysis
  Brainstorming Fishbone for understanding current situation and abnormality
  Preparation of material, resource for trail
  Prepare data for support problem hypothesis
A3 preparation
1
LEAN awareness training
2
Kaizen Leader, Co-leader Enhancement (if applicable)
3

## Slide 92
KAIZEN 3+1+3
Pre Kaizen Out Put
Educated members for LEAN implementation
A3 form, abnormalities Root Cause and LEAN Solution
Draft A3 submission to Crop BCID >= 10 days before Kaizen opening
Opening Presentation

## Slide 93
The appropriate pathway will facilitate the Kaizen team – Minimize “trial and error” but systematic planning
Approach thinking (not a solution) what is needed to achieve the Kaizen project target.
Based on kaizen project’s condition / scope
Deriving the Kaizen project approach

## Slide 94
Let’s Take an Example

## Slide 95
INCREASE STEAM PRODUCTION 55TON /HR @ $N / TON KAIZEN APPROACH FOCUS
(Increase boiler efficiency from N to Y)
Measurement error validation
Steam leakage
Incoming material condition
Preparation condition
SI, Biomass boiler efficiency inadequate
Steam supply to PM machine 55ton /hr at $N / ton (in term of volume and Quality)
Customer receive amount
Odor, Particle release
Public reaction
Technical control
What are the quality spec and what are the control to setup
Genba observation method of preparation. what are the specification and what are the deviation need to be improve
How the material been feed into boiler?
Genba analysis to observe What are the deviation against standard and hidden MUDA *
KaiZEN efforts changes on the process, method , design , system
What are the burning parameter setting , material burning composition ratio and what are the control
WHAT are the Benchmarking against boiler design efficiency?
WHAT are the equipment condition?
History data analysis identify the optimum setting condition
Trial run to be plan for KAIZEN
WHY WHY analysis on WHAT been identify (FACT, not perception )
LEAN approach solution idea
Kaizen week –week of action execution
APPROACH
Process flow mapping
Post -IT-tab marking (VA,VE,NVA)

## Slide 96
*MUDA aspect in identify abnormalities :
T How material been transfer feed
I What the impact of stock level to burning efficiency ?
M How the Material been prepare ?
W What are the material flow waiting happen or waiting of information reaction to burning process
O Steam venting respective elimination
O Over steam spec, additional step for managing incoming material
Defect Income material quality, boiler maintenance overdue, stem quality
Legend
Pre-Kaizen Week
Kaizen Week

## Slide 97
Let’s Take an Example

## Slide 98
REDUCE UNPLANNED DOWNTIME KAIZEN APPROACH FOCUS
Evolution effectiveness
Workshop repair performance
2
Repair plan
Evaluation effectiveness
2
Tool and part availability and quality
Store accuracy and storage condition
Breakdown maintenance execution Evaluation effectiveness
Minimize
Min Max analysis
optimize
Part
Management finance team procurement
Part
Evolution effectiveness
Evolution effectiveness
Evolution effectiveness
PVM-Periodic
Maintenance Plan
Breakdown data analysis (LPR)
PVM-Predictive
Maintenance
On the run planning Execution
Shut planning execution
Corrective Maintenance execution (NOT) just fixing, but improve )
Calibration flow
Skill matrix
Training
“Troubleshooting
Maintenance”
1
1
1
1

## Slide 99
Time | Day 1 | Day2 | Day 3 | Day 4 | Day5
8.00 am | Team pre ready | Recap briefing | Recap briefing | Recap briefing | Team Pre Ready
10.00 am | Kaizen event week opening presentation | Data analysis Solution Plan execution , Monitoring | Data Analysis Solution plan execution. Monitoring | Solution plan execution monitoring | Final presentation
12.00pm | Lunch Break |  |  |  | 
1.30 pm 3.00 pm | 1. kaizen approach sharing 2. VSM /process map/ Flow Chart /Block diagram focus discussion 3. Gemba walk observation focus | 1. Data Analysis 2. Solution Plan execution monitoring 3. Standard draft (Flow Chart) Action tasks list slide update | 1. Data Analysis 2. Solution plan execution Monitoring 3. Standard draft (Flow Chart) Action tasks list Slide update | 1. Solution plan execution Monitoring 2. Standardization 3. Control Mechanism Action tasks list , Slide update | Post Kaizen Plan integration into DM
4.00 pm | 4.Fishbone /WHY –WHY |  |  |  | 
 | Analysis finalization Solution Plan discussion | Kaizen leader meeting |  |  | 
KAIZEN 3+1+3
A
C
B
D
E
Plan and Share with team what and approach and why.
Must adequate been done to the actual root cause.
What are the action to ensure standard in place or what countermeasure action if Standard derive deviated?
Include all known action require to be focus in Post Kaizen
Knowing how to presenting the team efforts.

## Slide 100
MON
TUES & WED
THURS
FRI
Opening presentation (Morning)
Conduct Trial
Continue with action
Final Presentation
Finalize the analysis and focus to be execute
GENBA with validation
Update Action Plan
Leader’s Meeting (direction input sharing
Result tracking
Prepare closing presentation
Action List
Standardize
KAIZEN 3+1+3

## Slide 101
Integrate into Daily Management
Status List of Kaizen Actions
Persistent : Follow-up Kaizen action meeting
KAIZEN 3+1+3

## Slide 102
Spaghetti Diagram
Poka Yoke
Ergonomics principle
KANBAN
SMED
Visual Control
Brain Storming
Process Flow Chart
Value stream mapping
Ishikawa Diagram
Pareto
Histogram
Control Mechanism
Standard Work
1
3
2
4
Gemba & Observation
Analysis & Verification
Improvement Approach
Standardization
LEAN Tool

## Slide 103
Is a method for describing the whole set of activity process
Starting from receiving an order/order for a product services, from the customer
Until delivery to customers in the form of finished goods /information
VALUE STEAM MAP

## Slide 104
To identify which arear will focus based on a longest process time
to find out how the movement of information causes material , in terms of triggering and monitoring
to show the relationship and impact from the supplier to the customer
VALUE STEAM MAP FUNCTION

## Slide 105
Process flow
Material flow
Information Flow
Data Box
Value
Steam
Map
Component
Product /Service Process
Material movement, configuration , WIP
Enabling material flow : What , How, When Triggering
Details breakdown require in reflecting process current condition
1
2
3
4
OBJECTIVE
COMPONENT

## Slide 106
Information flow
Supplier
Central Controller
6 Weeks Forecast
90/60/30 day Forecast
Daily Order
Customers
Production Controller
MRP
Weekly Schedule
Tues. Thurs
I
I
A
I
B
I
C
I
D
I
E
SHIPPING
STAGING
Coins
5 Days
C/T = 10 sec
C/D = 1 hour
Uptime = B5%
27,600 sec avail
EPE = 2 Weeks
C/T = 39 sec
C/D = 10 mins.
Uptime = 100%
27,600 sec avail
2 shifts
C/T = 46 sec
C/D = 10 mins.
Uptime = 80%
27,600 sec avail
2 shifts
C/T = 62 sec
C/D = 0 mins.
Uptime = 100%
27,600 sec avail
2 shifts
C/T = 40 sec
C/D = 0 mins.
Uptime = 100%
27,600 sec avail
2 shifts
DATA BOX
NAV time
VA time
KAIZEN Brust
5 Days
1 Sec
7.6 days
1.8 days
39 Sec
42 Sec
2.7 days
62 Sec
40 Sec
4.5 Days
Production LT= 23.6 days
Processing time =188 Sec
VALUE STREAM MAP COMPONENT

## Slide 107
Is a Picture of Steps that are separate from a sequential work process.
PROCESS FLOW

## Slide 108
3 VERSION OF PROCESS FLOW
In any activities scope, there are 3 version of process flow
What you Think
What it Actually is
What it should

## Slide 109
SWIMLANE PROCESS FLOW

## Slide 110
It's a continuous flow line that use to identify redundancies in the work flow
To analyze and optimize the distances. the benefit can be either faster delivery or the same
delivery or the same delivery with less effort.
SPAGHETTI DIAGRAM

## Slide 111
Items to include in spaghetti diagram
layout & Work elements
Distance
Abnormalities
SPAGHETTI DIAGRAM

## Slide 112
Determine study area /Object
Get a color pen & layout of the area (prefer black & white)
Get consensus of the people observed /representative
follow the person on his daily work
record down starting time, ending time , abnormalities , travel .distance
Conduct analysis 7 come out idea for improvement
Spaghetti Diagram

## Slide 113
TIME STUDY

## Slide 114
What is Pareto Chart ?
A Pareto chart, named after Vilfredo Pareto, is a type of chart that contains both bars and a line graph, where individual values are represented on descending order by bars, and the cumulative total is represented by the line.
PARETO (80:20)

## Slide 115
Where to Use ?
When analysis data about the frequency of problems or causes in a process.
When there are many problem or causes and you want to focus on the most significant (80.20 Rules)
When communicating with others about your data.
PARETO (80:20)

## Slide 116
Decide what categories to group the items
Decide what measurement is appropriate eg. Frequency , Quality , Cost ,time etc
Decide what period of time the pareto chart will cover e.g Day, week , month
Collect data & sum up the measurement, calculate the percentage
Construct bars chart (from tallest to lowest)
Draw 2nd axis on accumulative percentage.
80%
20%
PARETO (80:20)

## Slide 117
Brainstorming combines a relaxed, Informal approach for LEAN Solution with lateral (sideway/crosswise) thinking.
It encourage people to come up with thoughts and ideas that can, at first, seem a bit crazy.
This helps to get people unstruck by “jolting” them out of their normal ways of thinking. Others can speak even more ideas.
BRAINSTORMING

## Slide 118
BRAINSTORMING
VS

## Slide 119
SILENT BRAINSTORMING : DONE WITHOUT DISCUSSION
Tools require
Pen Marker
Post it (Various Color)
Flip Chart

## Slide 120
Also name as cause & effect Diagram
The Ishikawa diagram identifies many possible. It can be used to structure a Brainstorming session.
it immediately sorts ideas into useful categories.
ISHIKAWA DIAGRAM

## Slide 121
ISHIKAWA DIAGRAM+5 WHYS
Mother Nature
Method
Machine
MAN
2nd Bone reflect to 1st bone on WHY
WHY 1
WHY 3
WHY 1
3rd bone reflect to 2nd bone on WHY
Measurement
Material
Use the categories
Use the statement
1st bone related to effect
Rules
Ask "Why " until it can't be asked anymore
Think about the root cause first , don't discuss solutions
Always focus on System Process > Tools > HUMAN

## Slide 122
WHY
WHY
WHY
Why my Tea is cold ?
Why the Boiler not heat up water ?
Why the circuit blow-up ?
Why wrong circuit been installed ?
Why the circuit specification not been determine?
Boiler not heating up the water
Not electric power, circuit blow -up
Wrong circuit been installed
Circuit require not been determine
No specification been given

## Slide 123
5 WHYS ANALYSIS

## Slide 124
Why come late for training Today ?
15- MINUTES EXERCISE

## Slide 125
Also known as mistake proofing, its a Japanese term meaning "avoiding inadvertent
mistake", which was formalized by Shigeo Shingo in 1961.
It's methos that either prevents error to occur , or making the mistake visible or detectable once occurring.
Proofing
ポカ
ヨク
POKA
YOKE
Mistake
POKA| YOKE

## Slide 126
POKA| YOKE
Forget
Misunderstand
Misidentification
Lack of Experience
Negligence
Lateness
Lack of Standardization
Shocked
Stubborn (don’t want follow the rules )
Deliberately (sabotage )
Not to blame, but think about what are the solution

## Slide 127
Detection /Warning System
POTENTIAL /CURRENT ABNORMALITIES
Perform root cause analysis
Can the solution become preventive
YES
NO
Prevention /Control System
POKA| YOKE

## Slide 128
EXAMPLE FOR CONTROL SYSTEM

## Slide 129
Smart Torque fastener to control tightening torque
Dual Palm push buttons to activate toggle press
Press cannot be activated when safety cover is opened
EXAMPLE FOR CONTROL SYSTEM

## Slide 130
Help to prevent or detect human (or machine error jidoka)
Promote safety and incident –free in the Workplace .
Improve quality of Product output and prevent delivery of detect to the customer.
Prevent damage of machine or property
Reduce cost of rework.
BENEFITS OF POKA YOKE

## Slide 131
SMED
SMED (Single -Minute Exchange of Dies ) is system for dramatically reducing the time it takes to complete equipment changeovers
Single-Minute Exchange of dies comes from the goal of reducing changeover times to the "Single" digit (i.e less than 10 Minutes).

## Slide 132
Last good product of RUN
First Good Product(s) of Run
30%
5%
50%
15%
A
B
Preparation
Actual Setup
Measurement & Setting
Adjustment /Trial Runs
Changeover Time
Changeover Time is the length of time from the last good product of a production run to the first good product(s) of the next production run
SMED

## Slide 133
Time Needed
CHANGEOVER
CHANGEOVER
EXTERNAL
CHANGEOVER
REMOVED
EXTERNAL
CHANGEOVER
REMOVED
EXTERNAL
STREAMLINED
Before
SMED
Separate
Convert
Streamline
SMED
STEP : 01
Identify target process.
Identify work elements of the process.
Separate external elements.
Convert internal elements to external as much as possible
Streamline remaining elements .
Internal Elements (elements that must be completed while the equipment is stopped)
External Elements (elements that can be completed while the equipment is running )
STEP : 02
STEP : 03
STEP : 04
STEP : 05

## Slide 134
Example

## Slide 135
SMED

## Slide 136
Lower manufacture cost (less equipment downtime)
Smaller lot sizes (faster changeover enable more frequent product changes)
Improved responsiveness to customer demand (smaller lot sizes enable more flexible scheduling)
Lower inventory levels (smaller lot sizes result in lower inventory levels)
Smoother start-ups(Standardized changeover processes improve consistency and quality)
SMED Benefits

## Slide 137
Visual control is the use of Signals, Lights, measurement, Diagrams, Charts & Sign to
Clearly define the normal or desired condition
Expose the abnormal undesired condition - real time
Enabling anyone visually
Understanding the current Situation (self-explaining)
Understand the Work Process (Self-ordering)
if You are ahead, behind or on schedule (Self-regulating)
When There is an Abnormality (Self-Improving)
VISUAL CONTROL

## Slide 138
Materials management
To find materials more easily and to return material more easily.
Material stock production level control.
VISUAL CONTROL FUNCTIONALITY

## Slide 139
VISUAL CONTROL FUNCTIONALITY
Remind people of safety information, and prevent unsafe condition.

## Slide 140
VISUAL CONTROL FUNCTIONALITY

## Slide 141
Blue : Project on time
Yellow : Project up to 0.5 hours behind >
current operations need to work faster
Red: Project greater than 0.5 hours behind > manager needs to bring in additional operators to help catch up
To motivate workers to achieve targets & qualities
VISUAL CONTROL FUNCTIONALITY

## Slide 142
VISUAL CONTROL FUNCTIONALITY

## Slide 143
VISUAL CONTROL FUNCTIONALITY

## Slide 144
VISUAL CONTROL FUNCTIONALITY

## Slide 145
VISUAL CONTROL FUNCTIONALITY

## Slide 146
KAN = "card" BAN = "Signal"
Is an information system that provides a signal to inform the need to start an activity
Control of production flow by providing information that connects the upstream and downstream processes at each level
Visualized "pull" system
Control inventory
KANBAN

## Slide 147
KANBAN – BIN SYSTEM
A system that uses a single bin or card to trigger an action
A 2-bin system is commonly used in storage areas at many types of workplaces.
A 3-bin system connects different departments or different parts of work processes

## Slide 148
2 CARD KANBAN
The first Kanban card, which moves between shipping and the store, is often called the withdrawal Kanban card.
The second Kanban card, which moves between the store and the production line, is often called the production Kanban card.

## Slide 149
SUPERMARKET
Parts Producing Process
KANBAN Card
Product with attached KANBAN Card
Product manufactured Item
KANBAN board
B
A
C
Parts Consuming Process
Supermarket

## Slide 150
Electronic KANBAN
Barcodes are placed on items, on materials, or in specific locations. These barcodes are scanned when more of something is needed, which sends a signal to the correct person or department to fill the request.
OTHER KANBAN

## Slide 151
Floor or Shelf Markings
Some workplaces or storage areas choose to use color- coded floor or shelf markings to indicate when something needs to be produced or ordered.
Green level, nothing needs to happen.
Yellow level, production might begin.
Red level, levels may have gotten too low and steps need to be taken to quickly fix the problem.
OTHER KANBAN

## Slide 152
Floor or Shelf Markings
Some workplaces or storage areas choose to use color- coded floor or shelf markings to indicate when something needs to be produced or ordered.
Green level, nothing needs to happen.
Yellow level, production might begin.
Red level, levels may have gotten too low and steps need to be taken to quickly fix the problem.
OTHER KANBAN

## Slide 153
OTHER KANBAN

## Slide 154
ERGONOMIC PRINCIPLE
Is a principle of tracing what work movements are the best, so that humans can work with highest performance and minimum levels of fatigue
Ease of movement of materials related to machines, tools, jigs (work aids), and layouts
Use free anergy such as gravity
Purpose:
Eliminating the causes of errors from work fatigue.
Trying to be able to work in rhythm by eliminating waste in terms of motion.

## Slide 155
MINIMIZE OVERALL MOVEMENT (COMBINE TASKS)
No. | Worker Movement
1 | Take Jig B
2 | Put Jig B into Machine
3 | Take Tool B from Rack
4 | Tighten Jig B with Tool B
5 | Put Tool B back on Rack
6 | Tool Jig A
7 | Put Jig A into Machine
8 | Take Tool A From Rack
9 | Put Tool A on machine
10 | Put pin into machine
11 | Take Tool A
12 | Tighten Jig A with Tool A
13 | Put Tool A back on Rack
No. | Worker Movement
1 | Take Jig Set A and B
2 | Put Jig set A and B Into Machine
3 | Take common Tools at machine
4 | Tighten Jig B
5 | Tighten Jig A
6 | Put common tools
13 - > 6
Worker-1

## Slide 156
USE BOTH HAND TO HANDLE
No. | Left hand | Right hand
1 | Take Jig set | wait
2 | Put Jig set into machine | wait
3 | wait | Take common tools
4 | wait | Tighten Jig B
5 | wait | Tighten Jig A
6 | Put common tools | wait
No. | Left hand | Right hand
1 | Take Jig set | Put comman t
2 | Put Jig set into machine | Tighten Jig B
3 | wait | Tighten Jig A
4 | wait | Release common tools
Worker-1
Worker-1

## Slide 157
ERGONOMIC PRINCIPLE

## Slide 158
ERGONOMIC PRINCIPLE

## Slide 159
ERGONOMIC PRINCIPLE

## Slide 160
STANDARD WORK

## Slide 161
STANDARD WORK

## Slide 162
STANDARD WORK

## Slide 163
3 ELEMENTS OF STANDARD WORK

## Slide 164
EXAMPLE OF STANDARD WORK

## Slide 165
EXAMPLE OF STANDARD WORK

## Slide 166
CONTROL MECHANISM

## Slide 167
LAT Summary

## Slide 168
LAT Summary